U.S. DEPARTMENT OF ENERGY

Office of Energy Assurance

ENERGY ASSURANCE DAILY

December 28, 2004

Highlights / Major Developments

# Thousands Still Without Power Across County

While a number of Licking County residents have regained power, 41,599 American Electric Power customers were still without electricity this morning. Current outage figures from the Energy Cooperative were not available Tuesday morning, but the organization reported 3,100 customers were without power as of Monday afternoon. In all, the storm knocked out power to more than 55,000 AEP and Energy Cooperative customers in Licking County at the height of the outages. Energy Cooperative Spokesman Brad Byrd expected 90 percent of customers who had originally lost power Thursday to be restored by midnight Wednesday. Some customers of both companies experienced a second power loss Monday due to a problem affecting a 69,000-volt transmission line near Utica.

According to Lisa Hooker, director of communications for South Central Power Co., about 18,000 of the company's customers were without power Monday afternoon. At the height of the outage Thursday, Hooker said, about 54,000 of the 105,000 customers South Central Power serves were without power. "It is our hope the bulk of these 18,000 people will have their service restored before (this) evening," Hooker said. "In the meantime, people will (gradually) continue to have their power come back on." Hooker estimates about 1,000 South Central customers in Lancaster are without power and about 6,200 customers in Canal Winchester and Pickerington combined do not have electricity. The rest of South Central Power's customers are in the Circleville and Hillsboro areas. American Electric Power also has electric customers in Fairfield County. According to company spokeswoman Vikki Michalski, 83,000 of AEP's 1.4 million customers in Ohio were without electricity Monday morning.

http://www.lancastereaglegazette.com/news/stories/20041228/localnews/1796792.html
http://www.newarkadvocate.com/news/stories/20041228/localnews/1797655.html

Electricity

Storm Knocks Out Power in Southern California
The Los Angeles Department of Water and Power (LADWP) reports that storm-related power outages have knocked out power for approximately 13,500 customers throughout Los Angeles, from San Pedro to the San Fernando Valley. http://home.businesswire.com/portal/site/altavista/index.jsp?ndmViewId=news_view&newsId=20041228005211&newsLang=en

East Coast Storm Delays Flights and Knocks Out Power
Tens of thousands of customers were left without power and at least three traffic deaths were blamed on the weather, one in Massachusetts and two in North Carolina. The storm's combination of wind, freezing rain and snow snapped tree limbs and power lines Sunday in the Carolinas. About 2,100 customers were still without electricity Monday in North Carolina, down from a peak of 14,000. More than 16,000 homes and businesses were blacked out Sunday in South Carolina, but that number was down to less than 5,000 Monday morning. Traffic resumed early Monday on Interstate 95 in eastern North Carolina after hundreds of travelers spent the night in hotel lobbies and shelters.
http://www.insidebayarea.com/news/ci_2499466

Storm Knocks out 36,000 Dominion Virginia Power Customers
http://www.wboc.com/Global/story.asp?S=2739483

# Powerful Pacific Storm Wallops California
Winds gusting more than 60 mph knocked out power to more than 80,000 customers in the Salinas area and briefly interrupted water service to about 30,000 residents on Monday. In the southern San Joaquin Valley, downed power lines left about 3,000 homes in Kern County without power Monday, Pacific Gas & Electric said.
http://www.nctimes.com/articles/2004/12/28/news/top_stories/13_42_1612_28_04.txt
http://www.newsday.com/news/nationworld/wire/sns-ap-california-storm,0,6919744.story?coll=sns-ap-nationworld-headlines

Sempra Calif. Elk Hills Power Plant Back

California-based energy company Sempra Energy's 549-megawatt Elk Hills  natural gas-fired power station in California returned to service by early Tuesday, the California Independent System Operator said in a report.  The station shut by late Monday.

Reuters 0722 December 28, 2004

# FirstEnergy Ohio Perry Nuke Up to 60 Percent Power

Ohio-based FirstEnergy Corp.'s 1,320-megawatt Perry nuclear station in Ohio ramped up to 60 percent of capacity by early Tuesday, the U.S. Nuclear Regulatory Commission said in its power reactor status report.  On Monday, the unit was operating at 25 percent of capacity after exiting an outage begun on Dec. 23 following a downshift of both recirculation pumps from fast to slow speed.

Reuters 1037 December 28, 2004

# TXU Texas Monticello Power Unit Shut, Seen Back Soon

Dallas-based TXU Corp. shut the 565-megawatt unit 2 at its Monticello coal-fired station in Texas on Dec. 27 to repair a boiler tube leak, the energy company told Texas regulators in a report.

Reuters 0806 December 28, 2004

# Ontario Lennox 2 Power Unit Shut, Seen Back Soon

Ontario Power Generation's 535-megawatt unit 2 at the Lennox oil- and natural gas-fired station in Ontario shut by early Tuesday for a short-term planned outage, a company spokesman said.  The unit was available for service but not necessarily operating on Monday.

Reuters 0837 December 28, 2004

# Exelon PA Peach Bottom 2 Nuke Dips to 67 Percent Power

Chicago-based Exelon Corp.'s 1,110-megawatt unit 2 at the Peach Bottom nuclear station in Pennsylvania dipped to 67 percent of capacity by early Tuesday for a rod pattern adjustment, a spokesman for the energy company said.

Reuters 0940 December 28, 2004

# FPL St. Lucie 2 Nuke Back Soon

In Florida, FPL expects its St. Lucie 2 nuke to start to exit an outage on Dec. 29. On Dec. 25, the company manually shut the unit due to an overheating in the condensate pump motor. The company replaced the motor and restarted the unit on Dec. 27. Later on Dec. 27, however, the company had to shut the unit again after it reached 10 percent of capacity due to a problem with a feedwater control system.
Reuters 1414 December 28, 2004

# Calpine’s 281 MW Gas-fired Delta Unit in CA Shutdown Dec 28
Reuters 1422 December 28, 2004

SCE’s 200 MW Coal-fired Mohave Unit 2 in NV Shutdown Dec 28
Reuters 1422 December 28, 2004

USBR’s  202 MW Hydro-powered San Luis Unit in CA Shutdown Dec 28

Reuters 1422 December 28, 2004

# FPL Fla. Turkey Point 4 Nuke Back at Full Power

Florida-based energy company FPL Group Inc.'s 693-megawatt unit 4 at the Turkey Point nuclear station in Florida returned to full power by early Tuesday, the U.S. Nuclear Regulatory Commission said in its power reactor status report.  On Monday, the unit was operating at 59 percent of capacity after exiting an outage begun on Dec. 25 due to lowering condenser vacuum.

Reuters 0719 December 28, 2004

New Jersey Orders 15-month Moratorium on Offshore Wind Projects
New Jersey Acting Gov Richard Codey (Democrat) has ordered a 15-month freeze on offshore wind projects while a panel studies the issue. An Executive Order dated Dec 23 acknowledges that wind could help relieve the state's reliance on fossil fuels and improve air quality, but notes that the "marine and coastal environment is an important natural resource [and]...an important economic and recreational resource," which must be protected. During the moratorium, the state will not provide permits or funding for any projects. One company, Winergy, has proposed a 350 MW project off New Jersey and Atlantic Renewable Energy has mentioned an interest in building a windfarm, but there are no operational projects..  http://www.platts.com/Electric%20Power/News/4254676.xml?S=n

Petroleum

# Shell Shuts Deer Park Unit

Royal Dutch/Shell’s 334,000 b/d Deer Park, Texas, refinery shut its olefins unit

Saturday, according to a report with the Texas Commission for Environmental

Quality. A leak on the compression and treating part of the plant caused the unit to shut.

Oil Daily, December 28, 2004

# Colonial Allocates Shipping 1st Cycle Mogas, Distillate

Colonial Pipeline on Tuesday announced allocations for shipping orders on its first cycle of 2005 for its main gasoline and distillate lines from Collins, Mississippi, to Greensboro, North Carolina, the company said.  It is the third straight 10-day cycle allocated for both distillate and gasoline products. The distillate line has had shipping limits since the 30th cycle, in late October.  As with previous allocations to shipping orders, demand to ship on the line outpaced space on the lines, said Steve Baker, Colonial spokesman.

Reuters 1013 December 28, 2004

Briefs

### Cold Hits Texas Refineries
Rare snow and freezing temperatures caused malfunctions at US Gulf Coast refineries in Texas over the long Christmas holiday weekend, according to reports filed on Monday with Texas environmental regulators.

Oil Daily, December 28, 2004

# Exxon Cuts Cat Cracker Feed at Beaumont, Texas Refinery

Exxon Mobil Corp. reduced the feed rate to the fluid catalytic converter at its 363,100 barrel per day refinery in Beaumont, Texas, on Monday, according to a company filing with state regulators.  The company reduced feed to the FCC because the refinery's High Pressure Carrier compressor shut due to the unexpected shutdown of steam producing boilers at the refinery's Power Plant 3.

Reuters 0854 December 28, 2004

El Paso Reaches Settlement with Arizona on Energy Crisis Lawsuits

El Paso Corp has reached a $46.4-mil settlement with Arizona over the state's pending litigation from the western energy crisis of 2000-2001, the company said Monday. The settlement has received final approval from the Maricopa County Superior Court, it added in a statement. As part of the settlement, El Paso is required to invest $43-mil in capital projects designed to improve

interstate pipeline service in Arizona, and accelerate $30-mil in already-planned pipeline integrity expenditures.
http://www.platts.com/Electric%20Power/News/7626946.xml?S=n

Saudi Oil Reserves May Increase

Saudi Arabia's oil reserves, the world's largest, could increase by almost 77 percent to top 461 billion barrels in a few years, the nation's oil minister said Sunday, December 26. " There are big chances

to increase the kingdom's producible oil reserves by 200 billion barrels," Ali Naimi said in a

statement issued after he inaugurated new oil fields in eastern Saudi Arabia. http://www.washingtonpost.com/wp−dyn/articles/A28101−2004Dec 26.html

# Rosneft Target Yugansk's Oil Output May Drop 40% on Power Cut

OAO Yuganskneftegaz, which accounts for 11 percent of Russia's oil production, may have to slash output because it faces power cuts after accumulating debt for

electricity supplies from a Siberia-based utility.

Bloomberg News, 0519 December 28, 2004

# Natural Gas

El Paso Plans $76M in Spending As Part of Arizona Settlement Deal 
El Paso Corp. will pay the state of Arizona $3.4 million, invest another $43 million in capital improvement projects in the state and accelerate $30 million in already-planned pipeline integrity expenditures as part of a settlement that received final approval from the Maricopa County Superior Court on Monday. The settlement covers pending litigation against the company from the western energy crisis in 2000 and 2001.  Natural Gas Intelligence, December 27, 2004

http://powermarketers.netcontentinc.net/newsreader.asp?ppa=8kowu%5DZkrsspjoYUmiw11rbfej%5B%21

FERC Clears Remaining Portion of Cheyenne Plains Pipeline for Service 
FERC on Thursday gave Cheyenne Plains Gas Pipeline Co., a subsidiary of El Paso Corp., the green light to begin service on the "remaining portion" of its 380-mile pipeline that transports natural gas from the prolific Rocky Mountain region to markets in the Mid-continent and Midwest.

Natural Gas Intelligence, December 27, 2004

http://powermarketers.netcontentinc.net/newsreader.asp?ppa=8kowu%5DZkrsspjoYUmiw11rbfej%5B%21

Most Cold-Related Pipe Constraints Fading; Freeze-Offs Reported 
With warming trends developing, several pipelines either had already canceled holiday restrictions that had been in effect over the long holiday weekend due to cold weather or were in the process of doing so. However, a few constraints were still in place Monday. Wellhead freeze-offs were reported in a couple of areas but did not affect deliveries.

Natural Gas Intelligence, December 27, 2004

http://powermarketers.netcontentinc.net/newsreader.asp?ppa=8kowu%5DZkrsspjoYUmiw11rbfej%5B%21

Nothing to report

Other News

Nothing to report.

Energy Prices

|  | Latest (12/28/04) | Week Ago | Year Ago |
| --- | --- | --- | --- |
| CRUDE OIL West Texas Intermediate US $/Barrel | 41.78 | 45.76 | 32.99 |
| NATURAL GAS Henry Hub $/Million Btu | 6.27 | 6.83 | 5.50 |

Source: Reuters

This Week in Petroleum from the Energy Information Administration (EIA)

http://tonto.eia.doe.gov/oog/info/twip/twip.asp

Updated on Wednesdays

Weekly Petroleum Status Report from EIA
http://www.eia.doe.gov/oil_gas/petroleum/data_publications/weekly_petroleum_status_report/wpsr.html

Updated after 1:00pm (Eastern Time) on Wednesdays

Natural Gas Weekly Update from EIA

http://tonto.eia.doe.gov/oog/info/ngw/ngupdate.asp

Updated after 2:00 pm (Eastern Time) on Thursdays